Western Europe – Western China International Transit Corridor Road reconstruction project

Lot-1(15) (1807 Km –1837 Km), Kyzylorda Bypass

Length: 28.4 Km (4-Lane)

Contractor: JSC "AzerKorpu"
Engineer: Dongsung Engg.
Amount of Contract: 8,722,196,588.00 tenge;
In 2010 - of 2013 Disbursement: 6 774 304 963,7  tenge;

Subcontractors:

LLP “Energomost”

Status of works as of 30.12.2013

| No. | Description | Total Contract | Achieved in 2010-2012 | Plan for 2013 | Actual in 2013 | Actual in percentage (%) | Delays |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Earth work, Thos. M3 | 3625 | 2303,81 | 1351 | 1230,26 | 91 | 120,7 |
| 2 | Sub base, km | 56,8 | 43,8 | 13 | 13 | 100 | 0 |
| 3 | Base course 20 cm, Km | 56,8 | 43,8 | 13 | 12,9 | 99 | 0,1 |
| 4 | Porous Asphalt, 12 cm, Km | 56,8 | 43,7 | 13,1 | 13 | 99 | 0,1 |
| 5 | Binder course 10 cm, Km | 56,8 | 42 | 14,8 | 14,6 | 99 | 0,2 |
| 6 | Wearing course, 5 cm, Km | 56,8 | 0,00 | 56,8 | 47,2 | 83 | 32 |
| 7 | Bridges, No. | 11 | 2(95%), 5(30%) | 11 | 10(75%)1(25%) | 70 |  |
| 8 | Culverts No | 20 | 17 | 3 | 19 | 95 |  |

| Material procurement | Plan for 2013 | Fact on 30.12.2013 | Performed.% | Remaining (+,-) |
| --- | --- | --- | --- | --- |
| 1 | Crushed stone thousand /ton | 231,03 | 231,03 | 100 | 0 |
| 2 | GSM thousand /ton | 86,7 | 123,4 | 142 | 0 |
| 3 | RCP thousand m3 | 0,93 | 0,93 | 100 | 0 |

Mobilization:

·	Mobilized 257 units of equipment, target 213 units

Personnel

Manpower has been involved in the number of 481 people, including:  Local staff – 421 people and International staff   – 60 people.

Amount of equipment required to perform the work program for 2013

| No | Name of equipment | Requirement | Actual | Additional required |
| --- | --- | --- | --- | --- |
| 1 | Dozer | 3 | 3 |  |
| 2 | Excavator | 20 | 14 |  |
| 3 | Loader | 5 | 6 |  |
| 4 | Rollers | 12 | 19 |  |
| 5 | Grader | 6 | 7 |  |
| 6 | Dumper | 90 | 104 |  |
| 7 | Paver | 2 | 3 |  |
| 8 | ACP | 1 | 1 |  |
| 9 | CCP | 1 | 2 |  |
| 10 | Crushing Plant | 2 | 1 |  |
| 11 | Others | 71 | 97 |  |
|  | Total: | 213 | 257 |  |