Western Europe – Western China International Transit Corridor Road reconstruction project

Lot-4  (1498 Km – 1578 Km)

Length: 80 Km (2-Lane)

Contractor: JSC «Salini Costruttori SpA»
Engineer: Isan Corporation / LLC "Zhol-Sapa"
Amount of Contract: 12,644,918 608.2 tenge;
In 2010 – 2013 Disbursement - 8 696 835 611,83  Tenge;

Subcontractors:

General Contractor “Salini Construttori” transferred according to the agreement to the Subcontractor organization “Standard Oil”, the technique rental agreement of "Sine Midas Story" LLP, “Beknur Momynai” LLP.

·	“Beknur Momynai” LLP signed a Contract with Salini on filling of approaches to the overpass PK 1728+25

·	"Mabeks" LLP signed a Contract with Salini for the works on REP PK 1236+50, currently works are not carried out.

Laboratory.

It is in village Tyuretam at 1570, it is 90% equipped. Roughmeter is in Kyzylorda.

As per work program

Status of works as of 30.12.2013

| No | Description | Total Contract | Achieved in 2010-2012 | Plan for 2013 | Actual in 2013 | Actual in percentage(%) | Delays |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Earth work, Thos. M3 | 1856,15 | 1112,63 | 451,08 | 301,07 | 67% | 105,8 |
| 2 | Sub base, km | 81,9 | 55,7 | 25,1 | 25,1 | 100% | 0 |
| 3 | Base course 20 cm, Km | 81,9 | 50,9 | 31 | 31 | 100% | 0 |
| 4 | Porous Asphalt, 12 cm, Km | 81,9 | 50,1 | 31,8 | 31,8 | 100% | 0 |
| 5 | Binder course 10 cm, Km | 81,9 | 39,7 | 42,2 | 42,2 | 100% | 0 |
| 6 | Wearing course, 5 cm, Km | 81,9 | 0 | 81,9 | 0,2 | 0% | 81,7 |
| 7 | Bridges, No. | 1 | 0,28 | 0,72 | 0,3 | 58% | 0,42 |
| 8 | Culverts No | 25 | 23 | 2 | 0 | 92% | 2 |

| Materials procurement | Plan for 2013 | Fact on 30.12.13 | Performed % | Remaining. (+,-) |
| --- | --- | --- | --- | --- |
| 1 | Crushed stone thousand/ton | 319,1 | 102,8 | 32 | 216 |
| 2 | RCP thousand. м3 | 0,88 | 0,62 | 70 | 0,26 |

Status of equipment for the execution of work program for 2013

| № | Description | Requirement | Available at site | Repairs | Additionally Required |
| --- | --- | --- | --- | --- | --- |
|  | Site PК 1000 – РК 1819 |
| 1 | Grader | 8 | 4 | 1 | 3 |
| 2 | Dozer | 10 | 6 | 1 | 3 |
| 3 | Excavator | 6 | 4 |  | 2 |
| 4 | Loader | 13 | 7 |  | 6 |
| 5 | Roller for earthwork | 13 | 5 |  | 8 |
| 6 | Roller for asphalt | 5 | 4 |  | 1 |
| 7 | Water tank | 8 | 2 |  | 6 |
| 8 | Paver | 7 | 2 |  | 5 |
| 9 | Milling machine | 1 | 1 |  | 0 |
| 10 | Crane | 1 |  |  | 1 |
| 11 | Dumper for technology | 115 | 32 | 1 | 82 |
| 12 | Asphalt plant | 3 | 1 | 1 | 1 |
| 13 | Others | 43 | 43 |  | 0 |
| Total | 233 | 111 | 4 | 118 |