Western Europe – Western China International Transit Corridor Road reconstruction project

Lot-5  (1578 Km – 1650 Km)

Length: 72 Km (2-Lane)

Contractors: Salini S.p.A Costruttori
Engineer: Kazdorproject

Amount of Contract: 11,694,768 539.90 tenge;
In 2010 - of 2013-Disbursement  11,930,987,925.39 tenge;

Subcontractors:

1.	LLP "Dorstroy" - For the 69.1 km of road works,

2.	LLP "SCI-Invest", “Mostospetsstroi-Astana” LLP  - to work on bridges and overpasses,

3.	 “Daryn-Zh” LLP  - For the construction of RES

Laboratory.

PC 646 is leftward bypass of village Zhosaly, it is 100%equipped.

Status of works as of 30.12.2013

| No | Description | Total Contract | Achieved in 2010-2012 | Plan for 2013 | Actual in 2013 | Actual in percentage (%) | Delays |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Earth work, Thos. M3 | 1642,3 | 1590,23 | 128,68 | 128,68 | 100% | 0 |
| 2 | Sub base, km | 69,1 | 65,5 | 3,6 | 3,6 | 100% | 0 |
| 3 | Base course 20 cm, Km | 69,1 | 65,5 | 3,6 | 3,6 | 100% | 0 |
| 4 | Porous Asphalt, 12 cm, Km | 69,1 | 65,5 | 3,6 | 3,6 | 100% | 0 |
| 5 | Binder course 10 cm, Km | 69,1 | 65,2 | 3,9 | 3,9 | 100% | 0 |
| 6 | Wearing course, 5 cm, Km | 69,1 | 40,5 | 28,6 | 28,6 | 100% | 0 |
| 7 | Bridges, No. | 4 | 2 | 2 | 0,3 | 58% | 1,7 |

| Materials procurement | Plan for 2013год | Fact on 30.12.2013 | Performed % | Remaining. (+,-) |
| --- | --- | --- | --- | --- |
| 1 | Crushed stone thousand/ton | 163,3 | 163,3 | 100% | 0 |
| 2 | GSM thousand/ton | 56,2 | 56,2 | 100% | 0 |

Status of equipment for the execution of work program for 2013

| No | Name of equipment | Demand | Actual | Additional required |
| --- | --- | --- | --- | --- |
| 1 | Dozer | 3 | 5 |  |
| 2 | Excavator | 7 | 6 | 1 |
| 3 | Loader | 9 | 7 | 2 |
| 4 | Rollers | 14 | 8 | 6 |
| 5 | Grader | 3 | 3 |  |
| 6 | Dumper | 105 | 31 | 74 |
| 7 | Paver | 5 | 3 | 2 |
| 8 | ACP | 2 | 2 |  |
| 9 | CCP | 1 | 1 |  |
| 10 | Crushing Plant | 1 | 1 |  |
| 11 | Others | 48 | 56 |  |
|  | Total: | 198 | 123 | 85 |

Personnel

The number of Personnel – 218 people, foreigner personnel – 7 people and local staff – 211 people.