Western Europe – Western China International Transit Corridor Road reconstruction project

Lot-10 (1877 Km –1917 Km)

Length: 40Km (4-Lane)

Contractor: JSC "Todini."
Engineer: Dongsung Engg.
Amount of Contract: 10,072,100 284.68 tenge;
In 2010 - of 2013 Disbursement: 9 012 562 896,25 tenge;

General Contractor is performing following types of work: sub grade construction, road pavement, culvert, construction of bridge on the 1878 km, furnishing of road;

Subcontractor: “Kazsevavtodor” LLP – sub grade construction, road pavement, culvert,

“Stroymost– 2010” - Construction of bridges on the 1899 km, 1915 km (right lane)

“Kerneu – SM” LLP – Construction of street lighting in Baygekum village – 100%

Status of works as of 30.12. 2013

Currently work performance corresponds to the current work schedule in the following quantity:

| No. | Description | Total Contract | Achieved in 2010-12 | Plan for 2013 | Actual in 2013 | Actual in percentage (%) |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Earth work, Thos. M3 | 1 396,2 | 1 277,6 | 118,6 | 117,5 | 99% |
| 2 | Sub base, km | 81 | 63,8 | 17,1 | 17,1 | 100% |
| 3 | Base course 20 cm, Km | 81 | 58,9 | 22,1 | 22,1 | 100% |
| 4 | Porous Asphalt, 12 cm, Km | 81 | 54,3 | 26,7 | 26,7 | 100% |
| 5 | Binder course 10 cm, Km | 81 | 50,1 | 30,8 | 30,8 | 100% |
| 6 | Wearing course, 5 cm, Km | 81 | 0 | 81 | 32,8 | 40% |
| 7 | Bridges, No. | 3 | 1,71 | 1,29 | 2,5 | 83% |
| 8 | Culverts No | 25 | 24,5 | 0,5 | 0 | 100% |
| 9 | Guard rails installation (r.m.) | 35 685 | 0 | 35 685 | 0 | 0% |
| 10 | Road signs installation (r.m) | 318 | 0 | 318 | 0 | 0% |

| Road construction material | Unit | Performed in 2010-2012 | Plan on 2013 | Procured 31.12.13 |
| --- | --- | --- | --- | --- |
| • Crushed stone (on the basis) | thousand tons | 200,2 | 82,2 | 80,0 |
| • Crushed stone for asphlat | thousand tons | 153,2 | 140,8 | 115,8 |
| •GSM | thousand tons | 494,1 | 104,5 | 104,5 |
| •Crushed Dust | thousand tons | 156,6 | 81,3 | 73,59 |
| • Cellulose additive for SMA | thousand tons | 0 | 371 | 149 |
| •Reinforced concrete products | m3 | 2,2 | 0,8 | 0,8 |
| •Cement | thousand tons | 0,5 | 0,4 | 0,4 |
| •Bitumen | thousand tons | 15,9 | 1,2 | 6,86 |
| •Mineral powder | thousand tons | 0 | 9,28 | 4,79 |
| •Curved bar | m | 0 | 35 685 | 0 |
| · Road signs | pcs | 0 | 318 | 318 |
| · Road marker post | pcs | 0 | 2350 | 2350 |

1.	Equipment mobilization of Lot 10:

Status of equipment for the execution of work program for 2013

| № п/п | Equipment | Lot 10 |
| --- | --- | --- |
|  |  | Plan | Fact |
| 1 | Road-building machine | 60 | 20 |
| 2 | Dozer | 3 | 2 |
| 3 | Excavator | 2 | 1 |
| 4 | Loader | 1 | 2 |
| 5 | Rollers | 9 | 8 |
| 6 | Grader | 2 | 2 |
| 7 | Dumper | 35 | 15 |
| 8 | Paver | 4 | 3 |
| 9 | Crane truck | 2 | 1 |
| 10 | Other | 5 | 5 |
| 11 | ACP | 2 | 2 |
| 12 | Bitum base | 1 | 1 |
| 13 | Dead-end track | 2 | 1 |
| 14 | Laboratory | 1 | - |

Notice: At the moment on the site there is not laboratory.