Western Europe – Western China International Transit Corridor Road reconstruction project

Lot-11 (1917 Km –1948 Km)

Length: 29 Km (4-Lane)

Contractor: Todini Costruzioni Generau
Engineer:  Roughton International
Amount of Contract: 9 431 788 899.02 tenge;
In 2010 -  2013: Disbursement 9 422 981 744,2 tenge;

Subcontractors:

1.	“Stroimost 2010” LLP  construction of overpass and artificial structures

Status of works as of 30.12.2013

| No | Description | Total Contract | Achieved in 2010-2012 | Plan for 2013 | Actual in 2013 | Actual in percentage (%) | Delays |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Earth work, Thos. M3 | 2161,48 | 2178,4 | 0 | 0 | 100 | 0 |
| 2 | Sub base, km | 58 | 58 | 0 | 0 | 100 | 0 |
| 3 | Base course 20 cm, Km | 58 | 57,1 | 0,9 | 0,9 | 100 | 0 |
| 4 | Porous Asphalt, 12 cm, Km | 58 | 56,6 | 1,4 | 1,4 | 100 | 0 |
| 5 | Binder course 10 cm, Km | 58 | 55,8 | 2,2 | 2,2 | 100 | 0 |
| 6 | Wearing course, 5 cm, Km | 58 | 5 | 53 | 53 | 100 | 0 |
| 7 | Bridges, No. | 2 | 1,85 | 0,15 | 0,1 | 97 | -0,05 |
| 8 | Culverts No | 36 | 36 | 0 | 0 | 100 | 0 |

| Material procurement | Plan for 2013 | Fact on 30.12.2013 | Performed.% | Remaining (+,-) |
| --- | --- | --- | --- | --- |
| 1 | Crushed stone thousand /ton | 47,5 | 47,5 | 100 | 0 |
| 2 | GSM thousand /ton | 61,1 | 61,1 | 100 | 0 |

Mobilization:

·	56 units of equipment have been mobilized (target 59 units), All equipment of Subcontractor “Kazsevavtodor”

·	Manpower has been engaged in the quantity of 280 people, including: Local staff – 254 people International staff – 26 people

Status of equipment for the execution of work program for 2013

| No | Name of equipment | Requirement | Actual | Additional required |
| --- | --- | --- | --- | --- |
| 1 | Dozer | 2 | 1 | 1 |
| 2 | Excavator | 3 | 2 | 1 |
| 3 | Loader | 4 | 3 | 1 |
| 4 | Rollers | 8 | 8 | 0 |
| 5 | Grader | 2 | 2 | 0 |
| 6 | Dumper | 28 | 28 | 0 |
| 7 | Paver | 3 | 3 | 0 |
| 8 | ACP | 2 | 2 | 0 |
| 9 | CCP | 1 | 1 | 0 |
| 10 | Crushing Plant | 1 | 1 |  |
| 11 | Others | 5 | 5 | 0 |
|  | Total: | 59 | 56 | 3 |