Western Europe – Western China International Transit Corridor Road reconstruction project

Lot-14 (Km 2012– Km 2057)

Length: 45 Km (4-Lane)

Contractor: Todini Costruzioni Generali
Engineer:  Roughton International
Amount of Contract: 8.747 billion  tenge;
In 2010 -  2013:Disbursement 11 175 484 378,9 tenge;

Subcontractors:

"SineMidaStroy" performs all works on the KM 2012 + 00 - Km 2057+00

Status of works as of 30.12.2013

| No. | Description | Total Contract | Achieved in 2010-2012 | Plan for 2013 | Actual in 2013 | Actual in percentage (%) | Delays |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Earth work, Thos. M3 | 1280,32 | 1280 | 0 | 0 | 100 |  |
| 2 | Sub base, km | 88,6 | 88,6 | 0 | 0 | 100 |  |
| 3 | Base course 20 cm, Km | 88,6 | 88,17 | 0,43 | 0,43 | 100 |  |
| 4 | Porous Asphalt, 12 cm, Km | 88,6 | 88,08 | 0,52 | 0,52 | 100 |  |
| 5 | Binder course 10 cm, Km | 88,6 | 88 | 0,6 | 0,6 | 100 |  |
| 6 | Wearing course, 5 cm, Km | 88,6 | 87,34 | 1,26 | 1,26 | 100 |  |
| 7 | Bridges, No. | 1 | 0,8 | 0,2 | 0,2 | 100 |  |
| 8 | Culverts No | 30 | 29 | 1 | 1 | 100 |  |

| Material procurement | Plan for 2013 | Fact on 30.12.2013 | Performed.% | Remaining (+,-) |
| --- | --- | --- | --- | --- |
| 1 | Crushed stone thousand / ton | 2,4 | 2,4 | 100 | 0 |

Mobilization:

·	36 units of equipment have been mobilized, target 113 units

·	Manpower has been involved in the number of 24 people, including:  Local staff – 10 people and International staff – 14 people,

Amount of equipment required to perform the work program for 2013

| No | Name of equipment | Requirement | Actual | Additional required |
| --- | --- | --- | --- | --- |
| 1 | Dozer | 7 | 2 |  |
| 2 | Excavator | 4 | 2 |  |
| 3 | Loader | 2 | 2 |  |
| 4 | Rollers | 10 | 0 |  |
| 5 | Grader | 3 | 2 |  |
| 6 | Dumper | 67 | 10 |  |
| 7 | Paver | 2 | 0 |  |
| 8 | ACP | 1 | 0 |  |
| 9 | CCP | 1 | 0 |  |
| 10 | Crushing Plant | 1 | 2 |  |
| 11 | Others | 15 | 16 |  |
|  | Total: | 113 | 36 |  |