Western Europe – Western China International Transit Corridor Road reconstruction project

Lot-6  (1650 Km –1702 Km)

Length :52 Km (2-Lane)

Contractor: JV "Akkord- Okan JV"
Engineer: Kazdorproject
Contract Amount: 8,802,684 950.55 tenge;
In 2010 - of 2013-Disbursement : 6,251,859,940.53 tenge;

Subcontractors: Subcontractor "Al Dekey" LLP for removal and relocating of existing communications and lighting of  transport interchange, additional equipment engaged by the leasing of equipment.

Laboratory.

PC 711 to the right of the road on the territory of the work site, it is 97%equipped.

As per work program:

Status of works as of 30.12.2013

| No | Description | Total Contract | Achieved in 2010-2012 | Plan for 2013 | Actual in 2013 | Actual in percentage (%) | Delays |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Earth work, Thos. M3 | 1028 | 844,56 | 351,49 | 351,49 | 100% | 0 |
| 2 | Sub base, km | 50,5 | 35,3 | 15,2 | 15,2 | 100% | 0 |
| 3 | Base course 20 cm, km | 50,5 | 30,2 | 20,3 | 20,3 | 100% | 0 |
| 4 | Porous Asphalt, 12 cm, km | 50,5 | 30 | 20,5 | 20,5 | 100% | 0 |
| 5 | Binder course 10 cm, km | 50,5 | 20,1 | 30,4 | 30,4 | 100% | 0 |
| 6 | Wearing course, 5 cm, km | 50,5 | 0 | 50,5 | 10,7 | 21,29% | 39,8 |
| 7 | Culverts No | 47 | 25 | 22 | 5 | 64% | 17 |
| 8 | Bridges, No. | 9 | 1 | 8 | 1,5 | 28% | 6,5 |

| Materials procurement | Plan for 2013 | Fact on 30.12.2013 | Performed % | Remaining. (+,-) |
| --- | --- | --- | --- | --- |
| 1 | Crushed stone thousand/ton | 178,6 | 170,22 | 95 | 8,3 |
| 2 | GSM thousand/ton | 239,85 | 235,5 | 98 | 4,4 |
| 3 | RCP thousand/ton | 0,38 | 0,38 | 100 | 0 |

Status of equipment for the execution of work program for 2013

| No | Name of equipment | Requirement | For December |
| --- | --- | --- | --- |
|  |  |  | Fact is on the site 30.12.2013 | Additional required |
| 1 | Dozer | 6 | 1 | 5 |
| 2 | Excavator | 5 | 3 | 2 |
| 3 | Loader | 10 | 7 | 3 |
| 4 | Rollers | 10 | 6 | 4 |
| 5 | Grader | 6 | 2 | 4 |
| 6 | Dumper | 104 | 34 | 70 |
| 7 | Paver | 5 | 2 | 3 |
| 8 | ACP | 1 | 1 | 0 |
| 9 | CCP | 1 | 1 | 0 |
| 10 | Crushing Plant | 1 | 1 | 1 |
| 11 | Others | 87 | 46 | 41 |
|  | Total: | 236 | 104 | 133 |

Personnel

The number of personnel - 232 people, foreign staff - 22 people and local staff - 210 people.