Western Europe – Western China International Transit Corridor Road reconstruction project

Lot 8 km 1752-km 1807 (Temirlan By-pass)

Length –                               14.843 km

Contractor                           «АКМ-Planum»

Consultant                   “Kazdorproject” LLP with Scott Wilson Ltd  & GZAMSHENPROJECT.

Commencement date          February 20, 2012

Contract Amount                6 577 777 777 KZT.

Advance payment               1 315 555 555 KZT

Disbursement in 2012: 2 000.32 million KZT

Disbursed in 2013 – 1 418 668 KZT

Subcontractors:

1. LLP " Kurylys" – Earth work.
2. LLP "MO-1" - performs the construction of the bridge.
3. LLP "Bereke CORPORATION-A" performs the construction of bridges.

Work performance as of 31.12.2013:

| No. | Description | Total Contract | Performance in 2012 | Plan for 2013 | Actual in 2013 | Actual in percentage (%) |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Earth work, embankment Thos. M3 | 1455,6 | 645,2 | 607,4 | 607,4 | 100 |
| 2 | Sub base, 33 cm, km | 28,6 | 7,6 | 21,7 | 27,7 | 100 |
| 3 | Base course CSGSM C-4, treated with cement Km | 28,6 | 4,7 | 23,9 | 20,6 | 86 |
| 4 | Concrete Pavement 27 cm, Km | 28,6 | 0 | 28,6 | 17,7 | 2% |
| 5 | Bridges & inter change No. | 8/100% | 6/70% | 6,3 | 6 | 97 |
| 6 | Culverts No | 20 | 14 | 8 | 8 | 100 |

Mobilization of Equipment

| No. | Name of equipment | Plan for 2013 | Actual at site | Additional required |
| --- | --- | --- | --- | --- |
| 1 | Dozer | 8 | 8 |  |
| 2 | Excavator | 8 | 8 |  |
| 3 | Grader | 9 | 9 |  |
| 4 | Loader | 9 | 9 |  |
| 5 | Roller | 14 | 11 |  |
| 6 | Dumper | 60 | 65 |  |
| 7 | Asphalt/Concrete Paver | 3/1 | 2/1 |  |
| 8 | Cement Concrete Plant | 3 | 3 |  |
| 9 | Others | 11 | 11 |  |
|  | Total | 110 | 127 |  |

Mobilization:

·	127 units of equipment have been mobilized target 110 units including Subcontractors equipment

·	Manpower has been engaged in the quantity of 420 people, including Subcontractors Local staff – 415 people and International staff –5 people

Reference: Earthworks. Earth works on the stage of completion. Ramping works  is carrying out.

Sub base on the main road is on the stage of completion. Material is transported all over the road. Works on sites between the bridges are implementing. At these sites remain grading operations.

Basis.

At the time on 13.12.13 laid 20.6 km from the project demand 28 6 km. Remaining - 8 km.

Cement concrete pavement. 17.6 km of pavement is laid by Contractor from 28.6 km. demand. Joint closure works is commenced.

Bridges and overpasses. Stage works of bridges and overpasses  - 95% completion. On four bridges are remained works on waterproofing facility and asphalt concrete pavement. From three overpasses, two as well have waterproofing and pavement, on one-PK 6+ 21 there are works on the bridge road bed facility.

At the moment, completed installation of all culverts on the project is completed by the Contractor - 20 pieces. Work on their strengthening are commenced.

Asphalt concrete works. The total demand-55 000 tons mixture. Bitumen BND 60/90 for the production -  2500 ton. Asphalt at the interchange and the existing road in the Temirlan village. "AKM-Planum" LLP intends to bring its resources.

Drainage channels. “KB Stroy” LLP are carrying out supply works and installation works of drainage channels. 2.0 km is set instead of required 9 km.

Lighting. Lightning work is commenced – stage new technical specifications.

Furnishing of road and road signs. Road signs, Constructor has established supply of signs with «KAZDORZNAK" LLP, Karaganda city. Barrier fencing will provide "TD Steel Zinc" LLP - demand 44 thousand running meter.