Western Europe – Western China International Transit Corridor Road reconstruction project

Shymkent – Border of Zhambyl oblast km 593-632

Value of the Contract: 15 751 627 460,00 tenge;

Contractor: General contractor: - SP «Dena Rahsaz & Sargin» (Iran/Turkey),

Engineer: CSC - Temelsu International Engineering Services Inc, in association with LLP "Consult LTD" (Turkey/Kazakhstan)

Commencement date – Notification about Commencement date was issued by Engineer 27.09.2013.

Disbursed in 2013 - 782 183,6 thousands tenge (planned for 2013 - 2 009,5 mln. tenge).

Subcontractors:

- LLP «Archeological expedition» was submitted for approval for work on archeological excavations.

Laboratory.

Laboratory of contractor is not functioning yet, it has not passed the certification and verification of devices, and there is no opportunity to test the RBM as well as control the road construction progress.

Work progress as of 30.12.2013

| № | Work description | unit | Total under Contract | Plan for 2013 | Actual | Performed% | Delays (+,-) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Earth work | thous. m3 | 2766,9 | 540,0 | 205,76 | 58,7 | -41,3 |
| 2 | Sub base | Km | 81,0 | 7,0 | 0 | 0 | -100 |
| 3 | Base course from CSSCM | Km | 80,6 | 7,0 | 0 | 0 | -100 |
| 4 | Pavement from cement concrete mix | Km | 80,6 | - |  |  |  |
| 5 | Bridges | pcs. | 3,0 | 0,2 | 0 | 0 | -100 |
| 6 | Overpasses | pcs. | 4,0 | - |  |  |  |
|  | Agricultural machinery passage | pcs. | 2,0 | - |  |  |  |
| 6 | Culverts | pcs. | 64,0 | 5,0 | 0 | 0 | -100 |

As of 30.12.2013

| Materials procurement | Total under Contract | Plan for 2013 | Actual | Performed % | Remaining (+,-) |
| --- | --- | --- | --- | --- | --- |
| 1 | Crushed stone thousand/m3 | 483,62 | 180.0 | 43,79 | 72,9 | -27,1 |  |
| 2 | GSM thous/m3 | 489,4 | 389.2 | 0.0 | 0.0 | -100 |
| 3 | Cement thous./тонн | 147.3 |  |  |  |  |
| 4 | Crusher dust thous. m3 | 43.5 |  |  |  |  |
| 5 | Sand thous. m3 | 105.3 |  |  |  |  |
| 6 | RCP, thous. m3 | 8.1 | 2.84 | 0,117 | 13,9 | -86,1 |
| 7 | Bitumen, thous. ton | 13.6 |  |  |  |  |

Equipment necessary for the execution of work program for 2013

| Name of equipment | Requirement | For year |
| --- | --- | --- |
|  |  | Mobilized | Additional required |
| Dozer | 4 | 2 |  |
| Excavator | 2 | 2 |  |
| Loader | 7 | 6 |  |
| Rollers | 8 | 13 |  |
| Grader | 3 | 4 |  |
| Dumper | 50 | 39 |  |
| Paver | 1 | 1 |  |
| CCP | 0 | 0 |  |
| Crushing Plant | 1 | 0 |  |
| Others | 3 | 3 |  |
| Total: | 79 | 70 |  |

Personnel

The number of personnel: overall 198 people, foreign staff - 36 people and local staff -162 people, including Subcontractors, machinery rental and RBM suppliers.