Western Europe – Western China International Transit Corridor Road reconstruction project

Lot-7  (1702 Km –1752 Km)

Length: 50 Km (2-Lane)

Contractor: "EVRASCON"
Engineer: LLP"Kazdorproject"
Amount of Contract: 8 144 812 972 tenge;
In 2013 Disbursement - 447 842 265 tenge;
The amount of work on 2014: 7 696 970 707  tenge;

Subcontractors: The General Contractor is planning to sign an agreement on subcontract for reconstruction of PTL - 35 kv

Laboratory.   Sample selection and core sample and their treatment, measurement and testing in accordance with the technical specifications of the Contract are processing for all kinds of work. The testing is processing in the laboratory LOT №15.

Status of works as of 30.12.2013

| No | Description | Total Contract | Achieved in 2010-2012 | Plan for 2013 | Actual in 2013 | Actual in percentage (%) | Delays |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Earth work, Thos. M3 | 1 282,292 | 1 282,292 | 57,239 | 116,3 | 0% | -10 |
| 2 | Sub base, km | 26,36 | 25,66 | 0,0 | 0,76 | 0,0% | 0 |
| 3 | Base course 20 cm, Km | 29,85 | 29,85 | 0,0 | 0,0 | 0,0% | 0 |
| 4 | Porous Asphalt, 12 cm, Km | 32,95 | 32,95 | 0,0 | 0,0 | 0,0% | 0 |
| 5 | Binder course 10 cm, Km | 47,89 | 47,89 | 0,0 | 0,0 | 0,0% | 0 |
| 6 | Wearing course, 5 cm, Km | 54,79 | 54,79 | 0,0 | 0,0 | 0,0% | 0 |
| 7 | Bridges, No. | 11 | 11 | 2 | 0,0 | 0,0% | 10 |
| 8 | Culverts No | 13 | 13 | 0 | 0,08 | 2% | 0 |

| Materials procurement | Total upon the Contract | Plan for 2013 | Plan for current date 30.12.13 | Fact on 30.12.13 | Performed % | Remaining. (+,-) |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Crushed stone thousand/ton | 406,312 | 406,312 | 24,595 | 12,06 | 2% | -10 |
| 2 | GSM thousand/ton | 383,803 | 383,803 | 22,899 | 3,331 | 0,8% | -15 |
| 3 | Chushed dust thousand/ton | 133,659 | 133,659 | 11,118 | 0,326 | 0,0% | -15 |
| 4 | RCP thousand. м3 | 2,890 | 2,74 | 0,00 | 1,92 | 66% | 0 |
| 5 | Bitumen thousand. / Ton | 13,568 | 13,568 | 0,00 | 0,0 | 0,0% | 0 |
| 5 | Cellulosic additives for CSMA, thousand / ton | 0,274 | 0,274 | 0,00 | 0,0 | 0,0% | 0 |
| 6 | Mineral powder thousand / ton | 7,304 | 7,304 | 0,00 | 0,0 | 0,0% | 0 |

Quantity of equipment required to perform the work program for 2013.

| Name | Demand for January 2013 | on 30.12.13 |
| --- | --- | --- |
|  |  | Fact is on the site on 30.12.13 | Additional required |
| Bulldozer | 3 | 2 | 1 |
| Excavator | 13 | 6 | 7 |
| Loader | 6 | 2 | 4 |
| Grader | 4 | 3 | 1 |
| Milling machine |  |  |  |
| Rollers | 8 | 5 | 3 |
| Paver |  |  |  |
| Dumper | 150 | 81 | 69 |
| Bitumen Distributor |  |  |  |
| Bitumen distributor |  |  |  |
| Water bawser | 1 | 1 |  |
| Fuel tanker | 1 | 1 |  |
| Crane | 2 | 5 |  |
| Car-pool | 8 | 5 | 3 |
| Buses | 3 | 2 | 1 |
| Law roader | 1 | 1 |  |
| Concrete mixer | 2 | 4 |  |
| Pile hammer |  |  |  |
| Cement carrier |  |  |  |
| Measuring machine |  |  |  |
| ACP |  |  |  |
| CCP | 1 | 1 |  |
| CSP | 1 | 1 |  |
| Total | 204 | 121 | 89 |

Personnel:

| Personnel | Lot №7 | % |
| --- | --- | --- |
|  | Plan | Fact |  |
| Overall personnel for January 2014 | 529 | 180 | 34% |