Western Europe – Western China International Transit Corridor Road reconstruction project

Lot-13 (1980 Km –2012 Km)

Length: 32Km (4-Lane)

Contractor: Todini Costruzioni Generau
Engineer:  Roughton International
Amount of Contract: 9,292,264,173.52  tenge;
In 2010 -  2013:Disbursement 10 556 097 648,97 tenge;

Subcontractors:

TOO "Storymost 2010" - the construction of overpass and artificial structures.

Status of works as of 30.12.2013

| No. | Description | Total Contract | Achieved in 2010-2012 | Plan for 2013 | Actual in 2013 | Actual in percentage (%) | Delays |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Earth work, Thos. M3 | 2299 | 2299 | 0 | 0 | 100 | - |
| 2 | Sub base, km | 64 | 64 | 0 | 0 | 100 | - |
| 3 | Base course 20 cm, Km | 64 | 64 | 0 | 0 | 100 | - |
| 4 | Porous Asphalt, 12 cm, Km | 64 | 64 | 0 | 0 | 100 | - |
| 5 | Binder course 10 cm, Km | 64 | 64 | 0 | 0 | 100 | - |
| 6 | Wearing course, 5 cm, Km | 64 | 64 | 0 | 0 | 100 | - |
| 7 | Bridges, No. | 1 | 0,99 | 0,01 | 0,01 | 100 | - |
| 8 | Culverts No | 18 | 18 | 0 | 0 | 100 |  |

| Material procurement | Plan for 2013 | Fact on 30.12.2013 | Performed.% | Remaining (+,-) |
| --- | --- | --- | --- | --- |
| 1 | Crushed stone thousand / ton | 5,5 | 5,5 | 100 | 0 |

Mobilization:

·	33 units of equipment have been mobilized, target 53 units.

Personnel

Manpower has been involved in the number of 30 people, including:   Local staff – 26 people and International staff – 4 people,

Status of equipment for the execution of work program for 2013

| No | Name of equipment | Requirement | Actual | Additional required |
| --- | --- | --- | --- | --- |
| 1 | Dozer | 2 | 1 |  |
| 2 | Excavator | 1 | 1 |  |
| 3 | Loader | 3 | 2 |  |
| 4 | Rollers | 3 | 3 |  |
| 5 | Grader | 2 | 2 |  |
| 6 | Dumper | 25 | 16 |  |
| 7 | Paver | 1 | 1 |  |
| 8 | ACP | 2 | 1 |  |
| 9 | CCP | 1 | 1 |  |
| 10 | Crushing Plant | 1 | 1 |  |
| 11 | others | 12 | 3 |  |
|  | Total: | 53 | 33 |  |