Western Europe – Western China International Transit Corridor Road reconstruction project

Lot-9 (1837 Km –1877 Km)

Length: 40Km (4-Lane)

Contractor: JSC "Todini."
Engineer: Dongsung Engg.
Amount of Contract: 10,027,324 453.70 tenge;
In 2010 - of 2013 Disbursement: 11,179,145,144.9 tenge;

Subcontractor:

1.TOO "Uad" – Arrangement of subgrade, pavement works, recreation areas, bus stops

2.”Triana Ltd” LLP – relocation of communications (PTL, communication lines, Fibre-Optical Communication Lines))

Status of works as of 30.12.2013

| No. | Description | Total Contract | Performed in 2010-2012. | Plan for 2013 | Actual in 2013 | Actual in percentage(%) | Delays |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Earth work, Thos. M3 | 1 442.97 | 1 435,97 | 6,998 | 6,998 | 100% | 0 |
| 2 | Sub base, km | 80 | 79,4 | 0,6 | 0,6 | 100% | 0 |
| 3 | Crushed stone base, km | 80.0 | 79,4 | 0,6 | 0,6 | 100% | 0 |
| 4 | Porous Asphalt, 12 cm, Km | 80 | 78,8 | 1.2 | 1.2 | 100% | 0 |
| 5 | Binder course 10 cm, Km | 80 | 78 | 2.0 | 2.0 | 100% | 0 |
| 6 | Wearing course, 5 cm, Km | 80 | 50 | 30 | 30 | 100% | 0 |
| 7 | Bridges, No. | 2 | 1.8 | 0,2 | 0,2 | 100% | 0 |
| 8 | Culverts No | 16 | 16 | - | - | - | 0 |
| 9 | Guard rails installation (r.m.) | 40,124 | 14,700 | 25,424 | 25,424 | 100% | 0 |
| 10 | Road signs installation (r.m) | 259 | 0 | 259 | 259 | 100% | 0 |

| Materials procurement | Plan for 2013 | Fact on 30.12.2013 | Performed % | Remaining. (+,-) |
| --- | --- | --- | --- | --- |
| 1 | Crushed stone thousand/ton | 20,2 | 20,2 | 100 | 0 |
| 2 | GSM thousand/ton | 1,9 | 1,9 | 100 | 0 |
| 3 | RCP thousand m3 | 0,003 | 0,003 | 100 | 0 |

Mobilization:

·	Mobilized 36 units of equipment, target 68 units (all equipment of Subcontractor UAD)

·	Manpower has been involved in the number of 122 people, including:  Local staff – 122 people,

Status of equipment for the execution of work program for 2013

| No | Name of equipment | Requirement | Actual | Additional required |
| --- | --- | --- | --- | --- |
| 1 | Dozer | 1 | 2 | 0 |
| 2 | Excavator | 1 | 2 | 0 |
| 3 | Loader | 1 | 1 | 0 |
| 4 | Rollers | 9 | 4 | 5 |
| 5 | Grader | 2 | 1 | 1 |
| 6 | Dumper | 35 | 10 | 25 |
| 7 | Paver | 4 | 2 | 2 |
| 8 | ACP | 2 | 2 | 0 |
| 9 | CCP | 1 | 1 | 0 |
| 10 | Others | 12 | 11 | 1 |
|  | Total: | 68 | 36 | 32 |